## Slide 1: Referee signals recognition in basketball
Pietro Fronza, Simone Compri

## Slide 2: Problem Description
Unfortunately, this job is not so simple, and the task is usually entrusted to the scorekeeper.
Very prone to error due to human interaction.
A common problem during a basketball match regards the timer management.
In fact, it should be stopped in response to some signals from the referee.

## Slide 3: State of the art

## Slide 4: Vision Based Referee Sign Language Recognition
Gesture feature divided in:
Static
  Hand feature extraction with Kinect
  SVM (with centroid distance) for hand posture classification (98,2% accuracy)
Dynamic
  Gesture scored against 11 HMMs (Referee CommLang)
Finite state machine for transitions between systems
Dataset: four users performing the set of commands in front of the camera

## Slide 5: Hand Signs recognition using ML and DL
Capturing gesture input
Pre-processing for noise reduction
  Face region identification
Relevant feature extraction
  Input -> Contour -> Centroid
Recognition models (cross validation and trained models)
  SVM
  CNN (4 convolutional layers and 2 fully connected)
Custom dataset created in real time
Results (accuracy)
 | ASL gestures | Action gestures
CNN | 97% | 93%
SVM | 84% | 80%

## Slide 6: Basketball Referee Signal
Recognition of basketball referee signals from real-time videos
Julius Žemgulys, Vidas Raudonis, Rytis Maskeliūnas, Robertas Damaševičius
Image preprocessing
Sobel operator for edge detection
Extraction of HOG features (image cropped to 128 x 64 pixels)
Extraction of LBP features
SVM for classification
For classification was used Region-Of-Interest.
Non-maximum suppression (NMS) to eliminate overlapping windows.

## Slide 7: Referee Signals recognition with wearable devices
Very high accuracy.
HOG and LBP for image segmentation.

## Slide 8: What we are going to do?

## Slide 9: ZED cam
Neural depth sensing
Ultrawide field of view with low distortions
Complete sensor stack
Thermal control
1
Simultaneos localization and mapping
2
Floor plane detection
3
Skeleton tracking

## Slide 10: Body tracking with ZED2
Focus on person’s bones detection and tracking
Build keypoints between bones
Implement body fitting
  recreates the skeleton based on the history of each tracked person to deduce missing keypoints

## Slide 11: MediaPipe
Suite of libraries and tools for you to quickly apply artificial intelligence (AI) and machine learning (ML) techniques
Core functionality:
MediaPipe Tasks: cross-platform APIs and libraries
MediaPipe Models: pre-trained, ready-to-run models
  MediaPipe Model Maker: Customize models

## Slide 12: Hand landmark detection with MediaPipe
Task based on the detection of landmarks of the hands in an image.
Input: image data with a machine learning (ML) model as static data or a continuous stream
Output:
Hand landmarks in image coordinates and world coordinates
Handedness(left/right hand) of multiple detected hands

## Slide 13: How the project will be structured

## Slide 14: Two phases
“Static” referee signal recognition
Signal recognition with the referee still in front of the camera.
The challenges regards the classification of several signals the referee can do to signal the table of what happened in the match.
“In game” referee signal recognition
Referee signal’s recognition in a game.
The challenges will be regarding the identification of the referee on the field and various occlusions due to the movements of the players.
In both cases the main base ideas are to use:
Capture gesture with a ZED 2 camera
Elaborate hand lanmarks with MediaPipe